## Slide 1
Presentation Title:
Session11
Presenter/Instructor:
Coordination Saves Lives
First Responder 2.0
Breaking/Cutting
<Name>
Coordination Saves Lives
Community Responder Training
Presentation Title:
Session 11
Presenter/Instructor:

## Slide 2: Breaking / Cutting
Community Responder Training
Coordination Saves Lives
  How to break through debris
  Effect on the debris
  Working in confined space

## Slide 3
Cutting and Breaking Operations
Avoid
move around, under or over the debris
if unstable, keep everyone at a safe distance
Move
if you can’t avoid it, move the debris
use gravity and the terrain to assist
Cut / Break
only if you cannot safely avoid / move the debris
measure and assemble props / shores in a safe place
secure the debris as you lift
use tools to develop the line of weakness until material breaks

## Slide 4
breach on an entry point where the work will go quick, without big efforts.
enter with a stretcher
make sure that the breaching work could be done at a brick row deeper if needed
be careful when loosing the first bricks
avoid parts from falling inside the opening (could be a risk for the victim)
Safety Considerations

## Slide 5
Always start with a stretcher course and with the middle brick of that stretcher course. The stretcher course are the lengthways bricks.
The Breaching Process
header course
stretcher course

## Slide 6
Continue with the other bricks in that row.
When completed start at the row above. Go on till the diameter is reached.
The Breaching Process
diameter

## Slide 7: The Breaching Process
Result: The hole should always be shaped like a „roof“.
most stable shape

## Slide 8
While working in the debris, void, building or wall:
avoid
secure the rescuer with a rope
never use open fire for illumination
don‘t do the hole in a load bearing wall
check the wall for fractures, or external load (debris, columns etc.)
Safety First!

## Slide 9: Entering the Building / Void
Entry of the rescuer:
The minimum size for the rescue hole is
30 cm (hight) 50 cm (width)
Be aware:
This measurement is valid for a small person without fear of narrow spaces!

## Slide 10: Entering the Building / Void
Using a stretcher
If the victim is injured and needs a stretcher for transportation, the minimum size of the rescue hole is:
40 cm (hight) 60 cm (width)
Notes: Use a folding rule to demonstrate how small the dimensions are

## Slide 11: Entering the Building / Void
Careful:
Those are minimum dimension!
Bigger victim / tool:
For special rescue tools or larger victims the rescue hole must be: 45 cm (hight) 70 cm (width)

## Slide 12
Questions
Cuestión
La question
الأسئلة
въпроси
问题
otázky
spørgsmål
vragen
küsimused
kysymykset
Fragen
सवालों के जवाब
pertanyaan
domande
質問
perguntas
вопросов
sorular
?