## Slide 1
Coordination Saves Lives
Community Responder Training
Disaster impact
<Name>
Presentation Title:
Session 02
Presenter/Instructor:

## Slide 2: Disaster Impact
Community Responder Training
Coordination Saves Lives
  Hazards
  Risks
  Dangers

## Slide 3: The post disaster situation: risky for rescuers
Community Responders have little training and no personnel protective equipment.
That is why you need to pay special attention to hazards, risks and dangers on-site.
The following slides show some examples.

## Slide 4: Damaged Infrastructure
Things to look out for
Missing street signs
Missing traffic control
No familiar landmarks
Loose power cables
Damaged or destroyed bridges
Blocked roads (for example through collapsed buildings and landslides)
Changed geography (different from maps)

## Slide 5: Damaged Utilities
Things to look out for
Gas leaks from broken pipes
  listen and smell!
Water from broken pipes
Sewage leaks (pollution)
Broken wires and cables
  assume they still hold electricity!
Broken telephone wires
  they can touch power cables that hold electricity

## Slide 6: Unstable Structures
Things to look out for
Aftershocks
Hidden holes and voids
Dust and plaster falling
Any movement of debris
Movement of walls, floors, columns or beams
  listen for creaking and groaning noises
Horizontal / vertical cracks appearing or widening

## Slide 7: Fire and Smoke
Things to look out for
Smoke is toxic and makes you unconscious very quickly
  avoid or reduce exposure
Debris or metal can be hot
  test surfaces with the back of your hand
Fire can cause explosions
  keep people outside of the danger zone
Heat can cause buildings to collapse

## Slide 8: Chemical Hazards
Things to look out for
Regular household chemicals
  when mixed they can become very dangerous
Gas cylinders
  smell!
Leaking batteries
  highly acid
Leaking chemical drums or tanks
Contaminated water with fuel & chemicals

## Slide 9: Environmental Hazards
Things to look out for
Contaminated water
  toxic and/or infectious
Body fluids of victims
Weather conditions
  cold or heat, high winds, snow, risk of flooding
Dust in the environment
  protect eyes, nose and mouth of rescuers and victims!

## Slide 10: Brainstorming:
You have 10 minutes to think about the following questions:
Which rules are important in a risky environment?
And which is the most important one?
... 10 minutes …
Notes: Max. 10 minutes!

## Slide 11: Brainstorming – possible results
Other rules are:
Never work alone
Don’t haste
Use all senses
Check twice before entering a structure / building
Protect yourself
…but most importantly: Safety First!
Be aware that your own safety is the key element for the rescue of victims.

## Slide 12
Questions
Cuestión
La question
الأسئلة
въпроси
问题
otázky
spørgsmål
vragen
küsimused
kysymykset
Fragen
सवालों के जवाब
pertanyaan
domande
質問
perguntas
вопросов
sorular
?